## Slide 1
ICCA OVERVIEW
Integrated Corporate Carbon Accounting (ICCA)
Assess both product and corporate carbon emissions with the rigor of financial accounting
casinitiative.org · 16 October 2026

## Slide 2
ICCA OVERVIEW
Integrated Corporate Carbon Accounting (ICCA)
Integrated Corporate Carbon Accounting (ICCA) · 16 October 2026
2
Direct
Emissions
Direct
Removals
Upstream
Emissions
CO2 Ledger
CO2 Balance
Sheet
Net CO2
Contribution
Net CO2
Flow
Product
Carbon
Footprints

## Slide 3
ICCA OVERVIEW
A Single CO2 Ledger
Integrated Corporate Carbon Accounting (ICCA) · 16 October 2026
3
Date
Activity
tCO2e
Scope
Debit (Destination)
Credit (Source)
T1
Machinery acquired
A
Scope 3.2
Machinery & Equipment
Upstream Emissions
T2
Raw materials purchased
B
Scope 3.1
Materials
Upstream Emissions
T3
Raw materials used in
production
C
Work-in-Process Goods
Materials
T4
Fuel combusted in production
D
Scope 1
Work-in-Process Goods
Direct Emissions
T5
Depreciation of machinery
E
Scope 3.2
Work-in-Process Goods
Machinery & Equipment
T6
Production of goods finished
F
Finished Goods
Work-in-Process Goods
T7
Electricity consumed
G
Scope 2
General & Admin. Emissions (Net CO2 Contribution)
Upstream Emissions
T8
Direct removals obtained
H
Direct Removals (CO2 Balance Sheet)
Direct Removals (Net CO2
Contribution)
T9
Finished goods sold
I
Carbon Emissions in Goods Sold (Net CO2
Contribution)
Finished Goods
T10
Net CO2 Contribution closed
out
J
Legacy Emissions
Net CO2 Contribution

## Slide 4
CO2 STATEMENTS: CORPORATE AND PRODUCTS
CO2 Balance Sheet
Integrated Corporate Carbon Accounting (ICCA) · 16 October 2026
4
CO2 Balance Sheet
Emissions in Assets
+
Buildings, Machinery & Equipment
−
A
E
+
Materials
−
B
C
+
Work-in-Process
−
C
D
E
F
+
Finished Goods
−
F
I
Source of Emissions
−
Direct Emissions
+
D
−
Direct Removals
+
H
−
Upstream Emissions
+
A
B
G
−
Legacy Emissions
+
J

## Slide 5
CO2 STATEMENTS: CORPORATE AND PRODUCTS
Net CO2 Contribution
Integrated Corporate Carbon Accounting (ICCA) · 16 October 2026
5
Net CO2 Contribution (Corporate Carbon Footprint)
Carbon Emissions in Goods Sold (CEGS)
I
+
General & Administrative Emissions
G
−
Direct Removals
H
=
Net CO2 Contribution (NCC)
J
+
Downstream Emissions Estimates of Goods Sold
=
Life-cycle Net CO2 Contribution

## Slide 6
CO2 STATEMENTS: CORPORATE AND PRODUCTS
Net CO2 Flow
Integrated Corporate Carbon Accounting (ICCA) · 16 October 2026
6
Net CO2 Flow
Direct Emissions (Scope 1)
D
−
Direct Removals
H
=
Net Direct Emissions (NDE)
+
Upstream Emissions (Scope 2 and 3)
+
+
A
B
G
=
Net CO2 Flow (NCF)
= Reading from Accounts for Reporting

## Slide 7
CO2 STATEMENTS: CORPORATE AND PRODUCTS
Product Carbon Footprint
Integrated Corporate Carbon Accounting (ICCA) · 16 October 2026
7
Product Carbon Footprint (PCF)
Partial
Full
Embodied
Emissions
+
+
C
D
E
+
+
C
D
E
+
General &
Admin.
Emissions
G
−
Direct
Removals
H
=
Product
Carbon
Footprint
(PCF)
I
J
+
Downstream
Emissions
Estimate
=
Life-cycle
PCF
= Reading from Accounts for Reporting

## Slide 8
RIGOROUS CARBON ACCOUNTING
Consistent Numbers
Integrated Corporate Carbon Accounting (ICCA) · 16 October 2026
8
Sum of PCFs of Products sold
+
General and Administrative Emissions
−
Carbon Credits
=
Net CO2 Contribution (Corporate Carbon Footprint)

## Slide 9
RIGOROUS CARBON ACCOUNTING
Reasonable Assurance
Integrated Corporate Carbon Accounting (ICCA) · 16 October 2026
9
Emissions in Assets
=
Upstream Emissions + Net Direct Emissions + Legacy Emissions
Δ Legacy Emissions
=
− Net CO2 Contribution
Net CO2 Flow
=
Net CO2 Contribution + Δ Emissions in Assets

## Slide 10
RIGOROUS CARBON ACCOUNTING
Strong Incentives
Integrated Corporate Carbon Accounting (ICCA) · 16 October 2026
10
Iron ore producer
Direct
=
PCF Iron
Steel producer
PCF Iron
+
Direct
=
PCF Steel
Body producer
PCF Steel
+
Direct
=
PCF Body
Car manufacturer
PCF Body
+
Direct
=
PCF Car
PCF Car
+
Downstream Indirect
=
Life-cycle PCF Car

## Slide 11
RIGOROUS CARBON ACCOUNTING
Lower Cost
Integrated Corporate Carbon Accounting (ICCA) · 16 October 2026
11
CO2 Ledger
CO2 Balance
Sheet
Net CO2
Contribution
Net CO2
Flow
Product
Carbon
Footprints
Integrated Corporate Carbon Accounting (ICCA)
ESRS
EPDs
EU ETS
CDP
CBAM
SBTi
CA SB253
TCFD
ISSB
…

## Slide 12
CASInitiative.org
Carbon Accounting Standards Initiative
JOIN THE INITIATIVE
The Carbon Accounting Standards Initiative (CASI) convenes academics, policymakers, and industry leaders to advance the practice of corporate carbon accounting and reporting.
Engage with CASI
christoph.ernst@casinitiative.org